## Slide 1: Nx CAST Tools Guide
Tools Overview & Setup Guide Quick References
03/18/2020

## Slide 2: Overview
What is this?
  Access Guide
    UNIX/EAM access procedure
    Source control setup (Perforce)
    Perforce directory structure
  Quick References
    “fulcrum”
    Digital Simulation (DSIM)
    Synthesis and P&R (proteus)
Who is this for?
  Nx Design & Flow Contributors
  NxSim Users
  NxSim Developers

## Slide 3: Nx Tools Overview
fulcrum | Master wrapper script. Used to access most tools. | In-house
nxsim | Matlab SNN modeling & verification framework | In-house
jdsim (Dsim) | Digital simulator optimized for asynchronous design | In-house
cast2verilog | Language translation utility (for simulation only) | In-house
supersize | Custom sizing flow shell | In-house
virtuoso | Custom layout editor (floorplanning) | Cadence
proteus | APR flow wrapper script (rdt, DC/ICC, etc.) | In-house
lve | Layout Verification Engine – wrapper script for layout verification | In-house
PrimeTime | Not (yet?) encapsulated inside LVE. | Synopsys
icv | Partially integrated inside lve, but commonly run externally. | Synopsys

## Slide 4: Account Access and Source Files
Unix groups (IEM approval) and Perforce account (EAM entitlement)
Project drive & working directory
Perforce setup

## Slide 5: Unix Account Access Guide
1) Nx Unix Accounts
  Use IEM to request access:
    http://iem2.intel.com/Default.aspx
  Nx Development Drive:
    fulcrum script
    Group: ncl@or
2) Set up Project Directory
  Using ION, log in for a VNC session
    Site: Oregon
    Group: /il/adr_sles11/vnc
  Create a working directory for yourself:
    /nfs/site/disks/or_lhdk75_disk0037/w137/gorda/<userid>
     Please maintain the consistent convention by using your correct “userid” string.
  Use the “pdx_normal” pool with –qslot=/ilabs/crl/short for any compute-intensive jobs.

## Slide 6: Perforce Access Guide
Perforce Access
  We use Perforce for versioning
    Tool source
    Nx Design source
    NxSim Source
  Request Access https://ags.intel.com/
    Access -> Submit Request
      Perforce NxWrite
      Perforce NxRead
      Perforce nxsim Write
      Perforce nxsim Read
      Perforce MRL Write
Perforce Info
  See www.perforce.com
  Also known as “Helix” (new name)
  We recommend you use the “p4” command from the unix prompt, although “p4v” gui is also available.
  Command quick reference (for p4v and p4): https://www.perforce.com/sites/default/files/pdf/p4-p4v-cheat-sheet.pdf

## Slide 7: Perforce Setup
# Make sure to add this in your .cshrc
# so that you don’t have to keep sourcing it
# every time you open a new terminal. You will
# need to adapt this if you use a non-tcsh shell!
source /nfs/site/disks/or_lhdk75_disk0037/w137/gorda/ncl/setup/project.user.csh
# Trust the connection to the perforce server
p4 trust
# Use your windows password
# The “-a” flag issues a ticket for
# all servers. Otherwise you will
# have to run p4 login on machine switch
p4 login -a

## Slide 8: Perforce Checkout
Nx Design Files
# Create Directory
mkdir –p /nfs/site/disks/or_lhdk75_disk0037/w137/gorda/$USER/p4/dev
# Set up .p4config
cd /nfs/site/disks/or_lhdk75_disk0037/w137/gorda/$USER/p4/dev
echo P4CLIENT=$USER-ncl-dev > .p4config
# Set up client, using sample client as template
# Save the client file that opens as .p4client
p4 client -t template-ncl-dev
# Sync your client space (this may take a while)
p4 sync
7nm Design Files
# Create Directory
mkdir –p /nfs/site/disks/or_lhdk75_disk0037/w137/gorda/$USER/p4/dev7
# Set up .p4config
cd /nfs/site/disks/or_lhdk75_disk0037/w137/gorda/$USER/p4/dev7
echo P4CLIENT=$USER-ncl-dev7 > .p4config
# Set up client, using sample client as template
# Save the client file that opens as .p4client
p4 client -t ppjoshi1-ncl-dev7
# Sync your client space (this may take a while)
p4 sync

## Slide 9: Relevant Perforce Directory Structure
NxSim (Legacy N1 structure, will change soon)
  p4/nxsim/n1{a,b,c}
    /core – Core NxSim Classes
    /experiments – Test code
    /misc – Miscellaneous helper scripts
    /projects – Test cases
  Currently, there is no n1a directory
Nx Design Files Relative to your client root: (p4/dev7/…)
  cast – HDL description of design
  spec – Sized gate netlists. Refines from base cell definitions under cast/ (usually autogenerated, mirrors cast/… hierarchy.)
  dfII – Virtuoso layout files
  spar – Synthesis/P&R collateral (library files, lef/def, etc.)
Many GB’s of data. Only check this out when you truly need it.
Not included in the “template-n2-cast” p4 client spec

## Slide 10: Environment Variable Conventions
$WORK_DIR | /nfs/site/disks/or_lhdk75_disk0037/w137/gorda/$USER
$CAST_DIR | Root of your “base cast” tree, i.e. $WORK_DIR/p4/dev/cast
$CAST7_DIR | Root of your “base cast” tree, i.e. $WORK_DIR/p4/dev7/cast
$SPEC_DIR | Root of your “spec tree”, i.e. $WORK_DIR/p4/dev7/spec
$DFII_DIR | Root of Cadence dfII layout tree, i.e. $WORK_DIR/p4/dev7/dfII
$SPAR_DIR | Root of spar collateral tree, i.e. $WORK_DIR/p4/dev7/spar
$CAST_PATH | Path for locating cast files. Typically $CAST7_DIR:$CAST_DIR:$SPEC_DIR

## Slide 11: CAST Source Directory Structure
lib/… | Generic library cells deeded for any non-trivial design project.
lib/util/* | Simple operators, flops, latches, etc. independent of any particular standard cell library.
lib/qdi/… | Library cells for Quasi-Delay-Insensitive asynchronous design (old)
lib/bd/… | Bundled Data asynchronous design primitives, e.g. controllers.
lib/bd/standard/* | Standard controllers and pipelining circuits for BD design.
lib/bd/6T/* | 6T SRAM designs, including multi-bank and pseudo-dual-ported designs.
lib/synchronous/… | Synchronous cells (not many), e.g. a TCAM and sync/async conversion cells.
lib/comb/ | Hand-optimized combinational logic agnostic to sync/async pipelining.
lib/metastable/… | Circuits designd to manage metastable centralized here (dangerous!)
vendor/… | IP imported from other providers, i.e. not developed in CAST framework.
vendor/intel/… | See d04.cast (d04 cell library), sram.cast (IDG SRAMs), IOs, etc.

## Slide 12: CAST Source Directory Structure
core/… | Modular self-contained blocks suitable for SOC integration.
core/neuro/… | Neuromorphic blocks. See base.cast, neuron.cast, mesh.cast, tile.cast.
core/neuro/neuron/… | N1* neuron design. N2 organization TBD (needs to support multiple cores).
core/noc/… | Lightweight NoC design for many-core mesh applications.
core/io/* | Off-chip interfacing cells, e.g. fpio.cast. (Interface logic, not pad drivers.)
chip/n1/* | N1 chip-level design definition
chip/n2/* | N2 chip-level design definition (not yet created).

## Slide 13: fulcrum Script

## Slide 14: Fulcrum Script Overview
Why use a wrapper script to run all tools?
  Users don’t have to worry about paths, versions, environment variables, etc. These are all handled behind the scenes for you.
  Standardizes the team’s tool flow usage conventions.
  Provides tool versioning for stability and debugging.
Main arguments:
  --pdk=<pdk> – Specifies the process PDK for relevant tools (1276 for N3)
  --latest – Use the latest (untested) tools build, advancing from the default released version. Use at your own risk!
fulcrum [--pdk=1276] [--latest] <tool> [tool-args…]

## Slide 15: DSim

## Slide 16: DSim: Digital Simulator aka “jdsim”
Arguments
  --cast-path – Specifies the source directories in search path priority order (leftmost is highest priority for search path), with colon (:) as the delimiter. Relative paths are accepted.
  --max-heap-size – Increases the JVM’s memory limit from its default. Needed when simulating large cells.
  --define=<var>:<value> – Overrides CAST metalanguage variables for various purposes.
To run gate-level simulations:
    fulcrum jdsim --cast-path=$CAST7_DIR:$CAST_DIR:$SPEC_DIR \
    --define=standard.attributes.standard_cell.USE_LIBERTY_PRS:true \
    --define=standard.attributes.bd_controller.ExtraTimingMargin:10000
fulcrum jdsim --cast-path=$CAST7_DIR:$CAST_DIR:$SPEC_DIR [--max-heap-size=2G]

## Slide 17: DSim: Simulating a cell
Arguments
  fully.qualified.cell.name – The cell to simulate (FQCN). Searches for the cell definition over the cast-path directories by looking for the following files:
      fully/qualified/cell.cast fully/qualified/cell/name.cast
  cosim-spec – Specifies which level(s) of FQCN to (co-)simulate. (Next slide.)
  env_name – one of the named test environments defined in FQCN’s env block.
Behavior
    By default, cosimulate loads both the highest level of design for FQCN as well as the lowest level of design, connecting both to env_name. During simulation, any discrepancies in behavior between the two models will be reported. (Just one level of modeling may be simulated, too – quite a common usage mode.)
Dsim> cosimulate fully.qualified.cell.name[{cosim-spec}]:env_name

## Slide 18: DSim: “Cosimulation Spec”
  {csp,subcells,prs} – Simulate the highest level of modeling (prefer csp if defined, otherwise descend to subcells, taking prs/transistor-level as a last resort.)
  {prs,subcells,csp} – Simulate the lowest level of modeling (prefer prs-subcells-csp in that order.)
  {N} – Descend N levels of hierarchy, then apply rule #1. {0} is equivalent to rule #1.
  {spec1|spec2} – Cosimulate FQCN{spec1} with FQCN{spec2} simultaneously, sending the same inputs to each and comparing their outputs. Example: {0|1}. Default: {0|prs,subcells,csp}
  spec1-exception_scope{spec2} – Applies a different cosim-spec to a scoped domain as an exception to spec1. exception_scope can be an instance name or a fqcn (attributes cells are common). Example: {prs,subcells,csp-standard.attributes.csp_model{csp}}
Dsim> cosimulate fully.qualified.cell.name[{cosim-spec}]:env_name

## Slide 19: DSim Common Commands: Cheat Sheet
reset
  Sets the top-level cell’s _RESET input to GND, simulates until the circuit is idle, then sets _RESET = VDD.
cycle
  Simulates the circuit. See ‘help cycle’ for different forms. Simulation can be halted with ^C.
devices
  Shows what csp processes are loaded in Dsim and what line/expression their execution is currently halted at.
quit or ^D – exits
csp <inst> get <var>
  Get the value of the variable <var> in the csp instance <inst>.
log_channels <inst> on/off
  Enable or disable printing the channel communications (input & output) of csp instance <inst>.
source <file>
  Read Dsim commands from <file>.
help and help <command>
  Many other commands available.

## Slide 20: Other DSim Commands (1)
For design debugging:
  get, set, watch – commands for node-level observation & setting
  haltonconflict, haltonerror, breakpt – Controls when ‘cycle’ halts
  fanin, fanout, aliases – queries circuit fanin/fanout/aliases of a particular node
  log, log_nodes, sst2 – For SST2 trace file logging (Simvision waveform viewer)
  __cosim_leftovers – reports status of cosim infrastructure channels
For coverage measurement
  csp_coverage – CSP statement coverage
  report_rule_coverage – PRS rule coverage

## Slide 21: Other DSim Commands (2)
For timing/performance measurement & debugging:
  timed_random, timed_delay – sets timing model (random, jittered, etc.)
  tcounts, trace, critical – To probe cyclic performance bottlenecks in a simulation
For post-layout simulation:
  get_switched_cap – capacitance-based dynamic energy estimation
  estimated_delay, measured_delay – enable accurate back-annotated timing models
For timing/performance measurement & debugging:
  timed_random, timed_delay – sets timing model (random, jittered, etc.)
  trace, critical – To probe cyclic performance bottlenecks in a simulation

## Slide 22: DSim FAQ
Can DSim simulate Verilog?
    No, but it can simulate synchronous designs at a gate level if they are imported to CAST. E.g. the PRS models of all g1m gates have been imported and can be found in vendor.intel.g1m.
  Is DSim the only way to simulate CAST designs?
    No, the cast2verilog tool can translate any CAST design into Verilog syntax suitable for simulation in VCS/NC-Sim/etc.
How does DSim deal with non-determinism in a cosimulation?
    This is the most complicated aspect of cosimulation. Most cells that we cosimulate in DSim are fully sequence-deterministic in their operation (i.e. given the same sequence of input tokens, regardless of timing, they will produce the same output tokens.) Non-determinism is introduced very carefully with arbiter cells (see lib.metastable.*). Arbiters use an advanced csp construct that allows DSim to link the arbitration decisions across multiple modeling levels during a cosimulation. The lowest-level model determine the arbiter decisions at upper levels.

## Slide 23: Proteus

## Slide 24: Synthesis, P&R (Proteus)
Directory Setup
  Write supersize scripts
  Run supersize to generate
    directory structure
    SPEC
    floorplan
    proteus.config
Proteus Tasks
  cast2rtl – Convert cast to synthesizable Verilog
  rdt_syn_setup – set up synthesis
  rdt_syn – run synthesis
  rdt_apr_setup – set up P&R
  rdt_apr – run P&R
  import-cast-after-syn – retrieve synthesis netlist for simulation
  import-cast-after-apr – retrieve apr netlist for simulation

## Slide 25: Sample Supersize Scripts (dev.in)
/nfs/site/disks/or_lhdk75_disk0037/w137/gorda/ncl/setup/supersize_example/scripts/dev.in
######################### path and perforce setup #########################
set USER = <userid>
set WD = /nfs/site/disks/or_lhdk75_disk0037/w137/gorda/${USER}
set CAST_DIR = ${WD}/p4/dev7/cast:${WD}/p4/dev/cast
set SPEC_DIR = ${WD}/p4/dev7/spec
set DFII_DIR = ${WD}/p4/dev7/dfII
set SPAR_DIR = ${WD}/p4/dev7/spar
set LEFDEF_DIR = ${WORK_DIR}/cds_wd
set P4_DFII_DIR = $DFII_DIR
set P4_CAST_CLIENT = ${USER}-ncl-dev7
set P4_DFII_CLIENT = ${USER}-ncl-dev7
set TAU = 16
set VTH = "c"
set DELAY_VTH = "c"
############################# alint setup #################################
set ASPICE_PERF_CORNERS = tttt:100:tttt:0.45:100,tttt:100:tttt:0.55:100,tttt:100:tttt:0.65:100,tttt:100:tttt:0.75:100,tttt:100:tttt:0.85:100,tttt:100:tttt:0.95:100,tttt:100:tttt:1.05:100,tttt:100:tttt:1.15:100
############################### options ###################################
set MEM = 4G
set LVE_JOBS = 16 # use lots of computers for lve
set size.sizable_delaybias = 1.00 # want accuracy here
set size.solve_hours = 0.01 # 0.6 minutes minimum effort
set size.max_solve_hours = 0.05 # 3 minutes maximum effort
set update_floorplan.fast = 1 # use much faster UpdateFloorplan
set CAST_DEFINES = < >
cast_server --refresh
setup_cdswd --user-template=${WD}/cdswd/template_1276

## Slide 26: Sample Supersize Scripts (mul.in)
/nfs/site/disks/or_lhdk75_disk0037/w137/gorda/ncl/setup/supersize_example/mul/mul.in
source ../scripts/dev.in
# Cell you’re trying to synthesize, append numeric subtype
set TOP = lib.bd.math.multiply.booth_csa.MUL(16,2,2,1,2).30000
# ABSTRACT representation of the cell you’re trying to synthesize
set PROTEUS_ABSTRACT = lib.bd.math.multiply.booth_csa.ABSTRACT_MUL
# Name to give to the synthesized/P&R’ed Cell (Must be different than above)
set PROTEUS_CELL = lib.bd.math.multiply.booth_csa.MUL_16_2_2_1_2.30000
set VTH = "c"
# create SPEC (Just run it. It’ll be fine)
create_subtypes
#Target g1m library
source ${SPEC_DIR}/release/g1m.in
query subcells --filter="!fixed&!leaf"
resubtype $query.result --reuse-spec=${SPEC_DIR}/release/bd_${VTH}.reuse
clean_subtypes --used --in-spec
clean_subtypes --unused
query subcells --filter="!fixed"
#Write proteus.config
proteus_config --lib=bd --scan-mode=off --runlocal=1 --task=syn

## Slide 27: Running Proteus
# Task list is comma separated
# Rightmost CLI flag overrides previous flags
# Launches proteus in netbatch
# --runlocal=1 forces a local run
proteus --include=proteus.config \
--task=<TASK>
Typical Tasks
  cast2rtl
  rdt_syn_setup,rdt_syn
  rdt_apr_setup,rdt_apr
  extract,pv
Directory Structure
  proteus/syn
  proteus/apr
  protues/extract
  proteus/pv