## Slide 1: CAST Tutorial
7/8/2024
Neuromorphic Computing Lab | Intel Labs

## Slide 2: Caltech Asynchronous Synthesis Tools
“CAST” Historically refers to an HDL developed at Caltech in the 90’s.
    Incorporates many concepts from advanced programming languages
    Optimized for asynchronous design, but supports synchronous too
    Further developed (much further) by Fulcrum Microsystems 2000-2011.
  We now refer to CAST as a full design flow spanning HDL to GDS
    Supports fully automated asynchronous bundled data (BD) design
    Supports full custom design of all styles (QDI, BD, synchronous, etc.)
    Ties many different tools (proprietary & commercial) into one framework
    By far the most advanced asynchronous design flow in the industry

## Slide 3: Why Another HDL?
Schematics
TCL
SystemC
Simics
Library
uArch
Circuits
Netlist
It is possible to represent asynchronous designs in Verilog.
  Peter Beerel (USC) has a SystemVerilog flow for async bundled data design
CAST is more than a different syntax
  A complete framework for efficient, productive HW design
  Was (and remains) ahead of its time. (E.g. Includes many features of Chisel, but much more concise than Chisel.)
File list
Verilog (RTL)
SystemC
RTL
(IP)
TCL
Verilog
(layout)
Verilog
(synth)
Verilog
(IP)
10-100K’s lines
1K’s lines
uArch
Arch
Circuits
Netlist
uArch
Circuits
Netlist
uArch
Circuits
Netlist
Verilog
SDC
TCL
etc.
Verilog
IP
Layout
Simics
SDC
CAST
Typical ASIC Front End
Schematics

## Slide 4: Intricacies of CAST
CAST is a meta-language which integrates many different sub-languages which describe circuits and test environments at many levels of abstraction.
In CAST, you would normally describe the hierarchical “box and arrow” structure of a circuit in a module.
These modules are often heavily parameterized to act as a “generator” of a circuit family (e.g. N-bit multipliers).
Files have *.cast suffix, and are organized by module name in a directory tree that follows the module name.
Contents from other modules can be imported with import commands, or referred to by a “fully qualified cell name” (FQCN) which includes the complete module and cell name with “.” separators. For example, lib.bd.math.add.ABSTRACT_ADD.

## Slide 5: DESIGN PHILOSOPHY

## Slide 6: Decomposition
Top-down decomposition process
  Start with high-level description
  Iteratively design partition into lower-level descriptions
  Use projection to formally map original description into subcells
  Use message-passing between subcells
Decomposition steered towards library cells:
    E.g., Logic functions, Arithmetic functions
    Crossbars, SRAMs, TCAMs
    Sometimes custom leaf-cells are needed
Performance & functionality checked at each stage of decomposition
Top Level
CSP
A
B
C

## Slide 7: Communication as a Primitive
Let X?u and Y!v be joined by a channel
Where u is a process variable, and
Where v is an expression of the same type as u.
The communication implements the assignment u = v
SENDER
RECEIVER
Y!v
X?u
Abstract Channel

## Slide 8: Communication at the circuit level
An asynchronous channel consists of
  A request “req”
  An acknowledgement “ack”
A req signifies the arrival of new data
An ack signifies the controller is ready to accept new data
All reqs/acks are bidirectional
  0->1 and 1->0 both infer a new token
Notes: 2-phase Bundled Data handshake with request and acknowledge wires
Datapath uses pos-edge latches
Clock is normally low, latches opaque
When token arrives on input (Lq!=La) and there is space on output (Rq==Ra), then raise the clock
After clock pulse delay, flip Rq and La
Similar to Click, except with latch instead of toggle, and stretched pulse-width
Routed as placeable hard macro
Timing LIB modified to eliminate loops

## Slide 9: Design Verification
Dsim: Digital simulator
  Designers write unit-level test environments in CAST, similar to verilog test-benches
  Simulations are run in Dsim, our equivalent of NCSIM/VCS
  Uses co-simulation to check that a lower-level implementation matches the higher-level specification
Design
Equivalence
Checker
Log
High-Level
Low-Level
Copy
Stimulus
Co-simulation Process
Async
Co-simulation
Chip-Level Verification
VCS
Verilog
DUT can be assembled from blocks at any level of decomposition
Verification
IP
Testbench
Interfaces
CSP
CSP
CSP
CSP
CSP
CSP
CSP
PRS/GATE
Digital
Co-simulation
Analog
Co-simulation
DSim
ASpice
XTOR
XTOR
XTOR
XTOR
Notes: Uses timing invariance of asynchronous circuits; tokenized values match on all external interfaces

## Slide 10: Automated Asynchronous design flow
Design Compiler (RDT)
CAST/CSP
(Design Source)
CAST2RTL
Compile
Retiming
Flop2Latch
ASYNC2SYNC
FPGA
LEC
ATPG
FC Compiler (Cheetah 2)
Place
CTS + Delayline
Route + Fill
ECO Loop
Extract
PT ECO
LV/RV Cleanup
Legend
Synopsys
Intel
proteus --include=design.config --task=spr,extract,pv --eco-iter=2 --lefdef-dir=./lefdef

## Slide 11: Async custom-library flows
Virtuoso
CAST/PRS
(Design Source)
Jauto Transistor sizing
cdl2lgf
Laygen
lgf2gds
LV/RV Cleanup
PDK
.sp
.lgf
.place
.lgf
.gds
Leaf cell flow
Virtuoso
FC
LV/RV Cleanup
.lef,.def
.gds
Mid-level “routing” flow

## Slide 12: Diving into CAST SYNTAX

## Slide 13: Structure of a CAST file
Module name
    Corresponds to location in directory structure
Import list
    Specify a list of other cast definitions to import
    Everything in standard.* is imported by default
Cell (aka circuit) definitions
    Defines the behavior of a cell and its environment
    Behavior can have many levels of abstraction
    Also includes directives for synthesis and simulation
Channel definitions
  Names a bundle of wires

## Slide 14: Example: lib/bd/math/add.cast
/** Synchronous adder **/
module ADD #(
parameter W = 32,
parameter WS = 33
) (
input wire CLK,
input wire [W-1:0] A,
input wire [W-1:0] B,
output reg [WS-1:0] S
);
reg [W-1:0] a, b;
always @ (posedge CLK) begin
a <= A;
b <= B;
S <= a + b;
end
endmodule
module ADD_env_digital();
parameter W = 32;
parameter WS = 33;
reg CLK;
reg [W-1:0] A, B;
wire [WS-1:0] S;
ADD #(.W(W), .WS(WS)) dut (
.CLK(CLK), .A(A), .B(B), .S(S)
);
initial begin
CLK = 0;
$monitor("%0t: S: %b", $time, S);
end
always
#5 CLK = !CLK;
always @ (negedge CLK) begin
A = $random;
B = $random;
end
endmodule
ADD
A
B
S
/** BD adder **/
module lib.bd.math.add;
define ABSTRACT_ADD(int W, WS)(bd(W) -A, -B; bd(WS) +S) {
csp { *[int(W) a,b; A?a, B?b; S!a+b] }
env {
digital {
subcells {
rsource_bd(W) _(A);
rsource_bd(W) _(B);
sink_bd(WS) _(S);
}
directives { ntpc_spec(S.C.q) = 36; }
}
}
}

## Slide 15: Synchronous adder circuit
/** Synchronous adder **/
module ADD #(
parameter W = 16,
parameter WS = 16
) (
input wire CLK,
input wire [W-1:0] A,
input wire [W-1:0] B,
output reg [WS-1:0] S
);
reg [W-1:0] a, b;
always @ (posedge CLK) begin
a <= A;
b <= B;
S <= a + b;
end
endmodule
CLK
A[15:0]
CLK
B[15:0]
CLK
CLK
S[15:0]
valueA
valueB
valueS
LOGIC

## Slide 16: Asynchronous adder circuit
/** BD adder **/
module lib.bd.math.add;
define ABSTRACT_ADD(int W, WS)(
bd(W) -A, -B; bd(WS) +S) {
csp {
*[int(W) a,b; A?a, B?b; S!a+b]
}
env {
digital {
subcells {
rsource_bd(W) _(A);
rsource_bd(W) _(B);
sink_bd(WS) _(S);
}
directives {
csp_time_inputs = 0; csp_time_outputs = 6; cycle_time = 10;
internal_slack = 1; //Retiming
}
}
}
}
CTRL
CLK
A[16:0]
Areq
Aack
CTRL
CLK
B[16:0]
Breq
Back
valueA
valueB
CLK
Sreq
Sack
S[16:0]
valueS
CTRL
LOGIC
C
SDC Constraints
Testbench

## Slide 17: Cell Definitions
define BUF()(bd(W) –L, +R){
    …
}
Type name
Has empty meta-parameter list
Has one input channel L and one output channel R, both of type bd with width W
Note: Module and cell name together specify a fully qualified name (FQCN)
  Ex: If module is lib.buffer, defines cell BUF, then the FQCN is lib.buffer.BUF

## Slide 18: Cell Definition details
define CELL_TYPE(metaparams)(ports)(implicit_ports) { contents }
CELL_TYPE has similar name restrictions as Verilog or C.
Metaparams is an optional list of int, bool, float which can be passed into this CELL_TYPE to change its implementation or behavior. Arrays of these are also allowed.
Ports is a list of node primitives or defchan channels. These are declared as “type pd1,pd2,…” sets separated by “;” whenever you need to change type.
Implicit ports are usually not specified, but are used to pass power supply nodes automatically down the hierarchy. There are no “global” nodes!
The contents are expressions of metaparameters plus sub-languages.

## Slide 19: Channel definition details
Ports of cells ultimately are the node primitive (a wire). Nodes in a port list can be input only, output only, or input-output as indicated by a -, +, or -+ prefix.
High-level CAST groups nodes into a channel of related nodes. For example, the bd(W) in the previous example is defined in module standard.channel as:
  defchan bdc()(node +q, -a) <: asynchronous_channel {}
  defchan bd(int W)(bdc +C; node[W] +D) <: asynchronous_channel {}
The “bdc” channel includes bundled-data handshake wires q and a, which is combined with an W-bit array of nodes to make a “bd(W)” channel.
The +/- directions are multiplied out to determine the ultimate input/output direction of each node. This is convenient because all asynchronous channels have nodes which travel backwards to provide flow-control.

## Slide 20: Refinement and Inheritance
Concepts borrowed from Object Oriented Programming for code reuse.
A CELL_TYPE can have only one refinement parent, indicated by <: PARENT_CELL_TYPE after the definition. This replicates everything from the parent, but allows the current cell to add more. Often, the parent is an ABSTRACT_CELL which defines only the functional behavior, while the refined cell adds a specific implementation.
A CELL_TYPE can inherit attributes from any number of attribute cells, indicated with by <+ ATTRIBUTE_CELL_TYPE. These can add CAST variables computed from metaparameters or reusable csp functions. Attributes cells are a special case of “define”.

## Slide 21: Iterators and Selection
The iterator:
<i:N:statement>;
Means evaluate the statement for each i from 0 to N-1. Alternatively: <i:lo..hi:statement>;
  Means evaluate the statement for each i from lo to hi.
  Also:
  [expression -> statement; ]
  Means if the metaparamter expression is true, then apply statement.
  CAST variables can be assigned only once!

## Slide 22: CAST Sub-Languages
csp { … } – CSP (Communicating Sequential Processes) is our behavioral language. It was adapted from Tony Hoare’s 1960’s language by Alain Martin at Caltech for describing the behavior of asynchronous components. Also referred as Communicating Hardware Processes (CHP)
subcells { … } – Subcells define the implementation of a cell in terms of smaller cells connected by nodes or channels.
prs { … } – PRS (Production Rule Set) is a powerful way of specifying combinational or state-holding or domino logic gates.
netlist { … } – Spice syntax for transistors. Usually auto-generated.
env { … } – Defines closed self-test environments for a cell. Supports csp, subcells, or prs specifications of the test environment.
verilog/java – Interfaces to external tools (seldom used these days).

## Slide 23: CSP

## Slide 24: CSP Block: Features
High-Level language to describe Asynchronous Circuits
Each cell is itself a csp program
    Each program typically runs indefinitely
    Each block communicates with other blocks via communication constructs on asynchronous channels
    Each block can be decomposed into fine grain blocks
    Eventually fine-grain blocks such that computation works on
      Arrays of channels making up 2 to 8 bits of data
      Data computation is computed in 2 gate-delays
      Forms pipelines with 10 transition cycle times
    Implemented with our cell templates (eg. BD)

## Slide 25: CSP Syntax: Variables and Constants
Syntax | Meaning
int x | Declare arbitrary precision integer
int(W) x | Declare W-bit unsigned integer
sint(W) y | Declare W-bit signed integer
bool b | Declare Boolean
int(W) x[0..N-1] | 1D array
int(W) x[0..A][0..B] | 2D array
true | Boolean true
false | Boolean false

## Slide 26: CSP Syntax: Statements and Expressions
Syntax | Meaning
skip | Dummy statement which does nothing
S1; S2 | Execute statement S1 then S2
S1, S2 | Execute S1 and S2 in parallel
(S) | Group a statement with higher precedence
v=E | Assign v to expression E
+ - * / % ** << >> log2(x) | Arithmetic operators
~ ¦ & ^ ¦¦ && | Bitwise/Boolean operators
== != < > <= >= | Comparison operators

## Slide 27: CSP Syntax: Communication and Flow Control
Syntax | Meaning
IN?v | Receive from input channel IN into v
OUT!E | Send expression E to output channel OUT
#CHAN | Probe if a channel is ready
#IN? | Peek the pending value of an input channel
[E] | Wait for expression E to be true
[E1 -> S1 [] E2 -> S2 ] | Wait for E1 or E2 then execute S1 or S2
[E1 -> S1 [] E2 -> S2 [] else -> S3] | If neither E1 or E2 is true, do S3
#[E1->S1 [] E2 -> S2] | If neither E1 or E2 is true, continue
*[E -> S] | While E is true execute S
*[S] | Repeat S forever

## Slide 28: CSP Syntax: Structures and Functions
structure struct_type = (int(3) x, y; sub_struct_type z);
Declare a structure variable with “struct_type struct_name”. Access fields with “struct_name::field_name”.
function func(int(4) –a, -b; struct_type -+z[10]) : type = (S);
Input parameters use “-”, outputs use “+”, in-out use “-+”. There are no pointers; inputs are copied to local variables upon entering the function, and outputs are assigned from local variables upon leaving the function.
The return type is optional and can be any variable type including a structure. To set the return value you assign to the name of the structure (”func=E”).
Functions are called as func(params) and can be used in expressions if they have a suitable return type.

## Slide 29: SUBCELLS

## Slide 30: Subcells Block
Subcells block is used to structure the decomposition
It contains node/channel/subcell instantiations
    All instantiations are private to this block
Subcells block cannot co-exist with PRS block

## Slide 31: SUBCELLS Deep-dive
/** BD multiplier **/
module lib.bd.math.multiply;
import lib.bd.math.add.ABSTRACT_ADD;
import lib.bd.source.bitgen.BD_BG;
import lib.bd.sink.bitbucket.BD_BB;
import lib.bd.standard.pipeline.*;
/** Abstract **/
define ABSTRACT_MUL(int W, COLS_PER_PIPE)(bd(W) -X, -Y; bd(2*W) +Z) {
csp {
*[int(W) x,y; X?x, Y?y; Z!x*y]
directives { internal_slack(Z) = (W-1)/COLS_PER_PIPE; }
} env {
digital {
subcells {
rsource_bd(W) _(X);
rsource_bd(W) _(Y);
sink_bd(2*W) _(Z);
}
directives { ntpc_spec(Z.C.q) = 36; }
}
}
}
MUL
X
Y
Z

## Slide 32
MUL_COLUMN_1
/** Multiplier core **/
define MUL(int W, COLS_PER_PIPE) <: ABSTRACT_MUL(W, COLS_PER_PIPE) {
subcells {
bd(W) a[0..W],b[0..W],x[0..W],s;
bd(1)[W] y,z;
BD_BG(W,0) bgA(a[0]);
BD_BG(W,0) bgB(b[0]);
x[0]=X;
BD_FORK(W) forkY(Y.C,{<,i:W:y[i].C>});
<i:W: y[i].D=Y.D[i]; >
<i:W: MUL_COLUMN_1(W,COLS_PER_PIPE,i)
col[i](y[i],z[i],x[i],a[i],b[i],x[i+1],a[i+1],b[i+1]); >
ABSTRACT_ADD(W,W) add(a[W],b[W],s);
BD_BB(W) bbX(x[W]);
BD_JOIN(W+1) joinZ({<,i:W:z[i].C>,s.C},Z.C);
<i:W: Z.D[i]=z[i].D[0]; >
Z.D[W..2*W-1]=s.D;
}
}
/** A 1-bit carry-save column **/
define MUL_COLUMN_1(int W, COLS_PER_PIPE, COL_NUM)
(bd(1) -Y, +Z; bd(W) -LX, -LA, -LB, +RX, +RA, +RB) {
int PIPE_NUM = COL_NUM/COLS_PER_PIPE; // which pipeline stage is this
int NUM_PIPES = (W+COLS_PER_PIPE-1)/COLS_PER_PIPE; // total number of pipe stages
csp {
*[int(1) y;
int(W) x,a,b,t;
int(W+1) s,c;
Y?y, LX?x, LA?a, LB?b;
#[y==1 -> t=x];
s=t^a^b, // sum
c=t&a|t&b|a&b; // carry
Z!s{0}, RX!x, RA!s>>1, RB!c
]
directives {
// pipelining
slack(Y) = PIPE_NUM+1; // pipelining from Y input
slack(Z) = NUM_PIPES-PIPE_NUM+1; // pipelining to Z output
[COL_NUM%COLS_PER_PIPE!=0 -> slack(LX)=0; slack(LA)=0; slack(LB)=0;] // no ripple input pipelining
slack(RX) = 0; slack(RA) = 0; slack(RB) = 0; // no ripple output pipelining
}
}
}
SUBCELLS Example
X
Y
Y
Z
Z
Z
MUL_COLUMN_1
ADD

## Slide 33: Subcells Syntax
Define nodes or channels:
  node x;
  node[16] y;
  bd(4) z1, z2[0..3],z3[0..1][0..2];
  Instantiate subcells:
  TYPE1(metaparams) inst1(ports1);
  TYPE2 inst2(ports2);
  TYPE3 inst3; inst3.port1=x; inst3.port2=y;
  Iterators and selection work in subcells body.

## Slide 34: DSIM

## Slide 35: Example: lib/bd/math/add.cast
/** Synchronous adder **/
module ADD #(
parameter W = 32,
parameter WS = 33
) (
input wire CLK,
input wire [W-1:0] A,
input wire [W-1:0] B,
output reg [WS-1:0] S
);
reg [W-1:0] a, b;
always @ (posedge CLK) begin
a <= A;
b <= B;
S <= a + b;
end
endmodule
module ADD_env_digital();
parameter W = 32;
parameter WS = 33;
reg CLK;
reg [W-1:0] A, B;
wire [WS-1:0] S;
ADD #(.W(W), .WS(WS)) dut (
.CLK(CLK), .A(A), .B(B), .S(S)
);
initial begin
CLK = 0;
$monitor("%0t: S: %b", $time, S);
end
always
#5 CLK = !CLK;
always @ (negedge CLK) begin
A = $random;
B = $random;
end
endmodule
ADD
A
B
S
/** BD adder **/
module lib.bd.math.add;
define ABSTRACT_ADD(int W, WS)(bd(W) -A, -B; bd(WS) +S) {
csp { *[int(W) a,b; A?a, B?b; S!a+b] }
env {
digital {
subcells {
rsource_bd(W) _(A);
rsource_bd(W) _(B);
sink_bd(WS) _(S);
}
directives { ntpc_spec(S.C.q) = 36; }
}
}
}

## Slide 36: Setup for jdsim (assumes csh syntax)
setenv MY_CAST_DIR $WARD/cast
setenv CAST_DIR /nfs/sc/proj/ctg/mrl108/amlines/hw/cast
setenv SPEC_DIR /nfs/sc/proj/ctg/mrl108/amlines/hw/731/spec
setenv FULCRUM /nfs/sc/proj/ctg/mrl108/mrl/tools/bin/fulcrum
alias jdsim '$FULCRUM jdsim --max-heap-size=1G --cast-path=${MY_CAST_DIR}:${CAST_DIR}:${SPEC_DIR}'
mkdir -p $MY_CAST_DIR/lib/bd/math
cd $MY_CAST_DIR/lib/bd/math
*jdsim is a digital simulator that supports CAST based designs

## Slide 37: To Simulate: jdsim
% fulcrum jdsim --cast-path=$CAST_DIR:$SPEC_DIR
cosimulate lib.bd.math.add.ABSTRACT_ADD(16,16){csp}:digital
devices
    *x
reset
timed_random
timed_delay 0.9 1
log_channels x on
cycle 2000
    1300: x: received 0x8001 on channel x.A
    1300: x: received 0x801d on channel x.B
    1300:x: sent 0x1e on channel x.S
    3100: x: received 0xd804 on channel x.A
    3100: x: received 0xa04b on channel x.B
    3100:x: sent 0x784f on channel x.S
help
Ctrl-C
Run DSim (aka jdsim)
Simulate the csp for ABSTRACT_ADD(16,16)
Prints all csp channel transactions
Cycle for 2000 time units (~1 cycle). During the cycle command dsim applies inputs and consumes outputs.
Press "ctrl-c" to halt the simulation. Executing "cycle" right after will continue the simulation from where it left.
Reset all variables to initial state

## Slide 38: Intricacies of co-simulation
cosimulate lib.bd.math.multiply.MUL(16,4){csp,subcells,prs|prs,subcells,csp}:digital
The { } is the “cosimulation spec” which says what levels you want to simulate.
The first says csp bodies take precedence over subcells or prs; “Highest level”.
The second says prs or subcells take precedence over csp; “Lowest level”.
The third says check the highest level against the lowest level. This is the default and may be omitted.
You can pass metaparameters to the name env as well, if it needs them.

## Slide 39: Other helpful DSIM tips
Print statements
Watching nodes
  The watch command in DSIM prints the time a signal changes along with its new value as the simulation proceeds.
Help
csp {
int size = 1 << (Z*log2(Y)); int xz,xb,xcin;
*[A?xa, B?xb, CIN?xcin; S!(xa+xb+xcin)%size, COUT!(xa+xb+xcin)/size;
print(0xa,xa);print(0xb,xb) ]
}
DSim> watch x.S.C.*
DSim> cycle
@1000 _env.S.C.q:1 (x. S.C.q)
@1300 _env.S.C.a:1 (x. S.C.a)
@1600 _env.S.C.q:0 (x. S.C.q)
@1800 _env.S.C.a:0 (x. S.C.a)
DSim> help
DSim> help watch

## Slide 40: Task 1: Create a new cell, add a targeted test
Create $MY_CAST_DIR/lib/bd/math/my_add.cast
Declare module and import ABSTRACT_ADD.
Define MY_ADD <: ABSTRACT_ADD with appropriate metaparams.
Add env { targeted { csp { … } } }
Write env CSP to send all possible input combinations to A and B.
Receive result back on S for each iteration.
Add debugging print(“A=“ + a + “ B=“ + b + “ S=“ + s);
Test in DSim with “cosimulate lib.bd.math.my_add.MY_ADD(4,4):targeted”

## Slide 41: ADVANCED DESIGN EXAMPLE: Mandelbrot set coprocessor

## Slide 42: What is the Mandelbrot set?
An infinitely complex fractal generated by a trivial bit of math as follows:
  For complex numbers Z and C
  Initially Z=0
  Iterate Z=Z2 +C
  End when |Z|>2 or after a maximum iteration count.
  Plot the C {real, imaginary} points where the max is reached.

## Slide 43: Module core.mandelbrot.abstract
/** Attributes for Mandelbrot engines, parameterized by bit width. **/
define mandelbrot(int W) attributes {
int W_TOP = 4; // bits above decimal point to represent -8.0 to 8.0
int W_ITER = 16; // bits of iteration counters
int SHIFT = W-W_TOP; // how much to downshift after multiplication
int SCALE = 2**SHIFT; // how much to multiply by to convert to fixed point
csp {
// single iteration of Mandelbrot set computation
function iterate(sint(W) -cr, -ci, -+zr, -+zi; int(W_ITER) -+iter) : bool =
(sint(W) zr_zr = zr*zr>>SHIFT;
sint(W) zi_zi = zi*zi>>SHIFT;
sint(W) zr_zi = zr*zi>>SHIFT;
zr = cr + zr_zr - zi_zi;
zi = ci + 2*zr_zi;
iter--;
iterate = iter==0 | zr_zr + zi_zi > 4<<SHIFT
);
}
}

## Slide 44: Review and Simulate
Read:
$CAST_DIR/core/mandelbrot/abstract.cast
Dsim:
cosimulate core.mandelbrot.abstract.ABSTRACT_MANDELBROT(32):mandelbrot_full(40,100)
Produces:
72002: _env:
144002: _env:
216002: _env:
288002: _env:
360002: _env:
432002: _env:
504002: _env:
576002: _env:
648002: _env:
720002: _env: *
792002: _env: ***
864002: _env: ***
936002: _env: * *******
1008002: _env: ************
1080002: _env: *************
1152002: _env: **************
1224002: _env: **************
1296002: _env: **** ***************
1368002: _env: *********************
1440002: _env: *********************
1512002: _env: * * ************************
1584002: _env: *********************
1656002: _env: *********************
1728002: _env: **** ***************
1800002: _env: **************
1872002: _env: **************
1944002: _env: *************
2016002: _env: ************
2088002: _env: * *******
2160002: _env: ***
2232002: _env: ***
2304002: _env: *
2376002: _env:
2448002: _env:
2520002: _env:
2592002: _env:
2664002: _env:
2736002: _env:
2808002: _env:
2880002: _env:

## Slide 45: Synthesizable CSP
There are many restrictions on CSP to be synthesizable.
Inner loops are unrolled at synthesis time, so cannot take a variable number of iterations. To avoid, rewrite as a single outer loop with case statements based on a new state variable to distinguish what to do on each cycle.
Each channel can only be sent/received 0 or 1 times per outer loop. Again, the solution is to rewrite as a state machine with explicit “cycles”.
Also important to declare variable widths. Otherwise it assumes 129 bits and may or may not be able to optimize out unused bits.
Some functions are features of CSP are not synthesizable. Strings, asserts, print, etc.

## Slide 46: Task 1: Synthesizable Mandelbrot Engine
Define cell BASE_MANDELBROT <: ABSTRACT_MANDELBROT in a new module.
Add a subcells body and instantiate CORE_MANDELBROT in it.
Define CORE_MANDELBROT with synthesizable CSP.
Cosimulate BASE_MANDELBROT to test correctness.
Note that you can’t refine a cell to add new CSP if the parent already has CSP. That’s why we have to put CORE_MANDELBROT in a subcell instead. Confusing!

## Slide 47: Task 2: Decompose to be more optimal
Although synthesizable now, the design will literally synthesize to 3 multipliers and 4 adders and 1 comparison of fixed-point numbers, plus some additional logic for iter and done.
This is quite large, and will not run fast because of the data dependency from one cycle to the next.
Instead, import lib.bd.math.multiply.ABSTRACT_MUL and add a single instance of this in CORE_MANDELBROT’s subcells body.
Remove all the a*b>>SHIFT statements from the CSP and instead send the operands on channels to the ABSTRACT_MUL and receive the result.
You can do this edit locally as a “remote procedure call”.

## Slide 48: Task 3: Optimize the RPC
However, an RPC creates a difficult to synthesize performance bottleneck. It will try to receive the results of the multiplies in the same cycle it sends the operands.
It is better to receive the results on the next cycle instead. Use state variables to defer the receive of the product until the cycle after you send the operands to the multiplier.
Try to compute the adds and compares as soon as you have enough information.
You will need more state variables in CORE_MANDELBROT to hold temporary data.
Also rewrite your state machine to send and receive at most 1 token on the channels to the multiplier per outer loop.
Now you should have something which is reasonably optimized and synthesizable!

## Slide 49: Run APR
proteus \
--abstract=core.mandelbrot.abstract.ABSTRACT_MANDELBROT(32) \
--base=core.mandelbrot.base.BASE_MANDELBROT(32) \
--cell=core.mandelbrot.base.BASE_MANDELBROT.1000

## Slide 50: Task 4: Use a soft-macro multiplier
Create SOFT_MANDELBROT <: BASE_MANDELBROT
Add:
subtypes { ABSTRACT_MUL(W,W,W,SHIFT,1) :> MUL(W,W,W,SHIFT,1) mul;
}
This refines the multiplier instance from synthesizable CSP to a soft-macro design.
This will take more work to run through proteus because we need to use Supersize to choose what subtypes to use for the soft macros. TBD.